## Slide 1
Student:
Student Email:
Faculty:
Faculty Email:
AFRL Sponsor:
AFRL Directorate:
An Investigation of Detonation Diffraction, Reinitiation, and Amplification
Benjamin Millard
millarbm@mail.uc.edu
Dr. Daniel Cuppoletti
cuppoldr@ucmail.uc.edu
Dr. Timothy Ombrello
AFRL/RQ
PA #:
AFRL-2022-4748

## Slide 2
Continuing work into pulsed detonation ignition devices conducted by Dr. Ombrello
Exploration of a detonation amplification behavior as a potential means to augment a given detonation ignitor performance
End goal is to integrate into a scramjet combustor to achieve more reliable ignition for low residence time and low enthalpy conditions
Introduction
Rosato et. al

## Slide 3
Project consisted of two stages
  The first stage consisted of characterizing the dependence between the amplification behavior and the detonation cell size
    This was achieved by controlling the reaction mixture equivalence ratio and testing with three different fuels, CH4, C2H4, C3H8
    Detonation propagation capture using pressure and ion probes to measure the propagation of the shock front and flame front respectively
  The second stage follows up on the first by using high-speed imagery to spatially resolve the detonation amplification process
    An optically accessible detonation chamber was designed and manufactured to facilitate Schlieren and Chemiluminescence Imagery of the detonation phenomenon
Testing

## Slide 4
The initial testing found 3 unique detonation behavior
  The first is a spike amplification behavior where the detonation amplifies in the middle of the detonation chamber that is accompanied by a spike in pressure impulse
  The second had the same middle of the chamber amplification but without a significant spike in pressure at the initial amplification event
  The third is an end wall amplification event where the detonation is amplified due to effects from the end wall of the detonation chamber resulting in a heavily amplified outlet
Stage 1

## Slide 5
Inlet Pressure
Decoupled Detonation
Rapid Attenuation
Still-Amplified Outlet
Amplified Spike
Localized Wall Reinitiation
Spike Amplification

## Slide 6
Steady Amplification
Inlet Pressure
Slower Attenuation
Still-Amplified Outlet
Recoupling Spike

## Slide 7
Endwall Amplification
Inlet Pressure
Highly Amplified Outlet
Double Spike Indicating A Decoupled Detonation

## Slide 8
Stage 2
Stage two involved developing an optical accessible 2 in. square detonation chamber capable of withstanding an amplified detonation
The mechanism behind two of the three behaviors documented in stage 1 where captured
  The steady amplification behavior was not able to be reproduced due to the large area of the 2 in. square section
Schlieren and CH* Chemiluminescence imagery was taken in the same field of view using two Shimadzu HPV-X2 camera’s
  Camera operated at 500,000 FPS with a frame size of 400 by 250 pixels

## Slide 9
Spike Amplification
C2H4-N2O Equivalence Ratio=1.0

## Slide 10
Endwall Amplification
CH4-N2O Equivalence Ratio=1.0