## Slide 1
Student:
Student Email:
Faculty:
Faculty Email:
AFRL Sponsor:
AFRL Directorate:
Multiscale Modeling of Composite Materials with the Generalized Finite Element Method
Bryce Mazurowski
brycepm2@Illinois.edu
Prof. C. Armando Duarte
caduarte@Illinois.edu
Dr. Patrick O’Hara
AFRL/RQHF
Distribution Statement A: Approved for public release;
Distribution is unlimited. PA# AFRL-2022-4599 .

## Slide 2
Pros
High strength-to-weight ratio
Temperature resistant
Stable mechanical properties
Ductile behavior
Cons
Very heterogeneous material
Seeded with defects
No separation of length scales at hot spots
Ceramic Matrix Composites
How to incorporate heterogeneity into global structure behavior efficiently?
Valkyrie – Boeing hypersonic concept vehicle

## Slide 3: Generalized FEM
Augment standard FEM space with enrichment functions
Introduce solution features directly to approximation space
Remove meshing restrictions
GFEM Applications
  Fracture Mechanics
  Material discontinuities
  Contact
  Porous media

## Slide 4: Proposed GFEMgl
Global:
Coarse solid mesh
Homogenized material
Local:
Fine solid mesh
Heterogeneous material
Microstructure-informed damage models
GFEMgl establishes two-way communication between the global and local scale
Material heterogeneity and nonlinearity incorporated only at localized hot spots

## Slide 5: Example Problem Geometry - Plate With a Hole
Reference Mesh
GFEMgl Global Mesh
Goal: Recover same fidelity in local region as fine reference mesh using coarse global mesh

## Slide 6: Plate With a Hole Under Tension
CMC
Fiber Comp.
Fiber Comp.
GFEMgl recovers local measures accurately
Submodeling does not
Expected failure
Plots of stress concentration through-the-thickness

## Slide 7: Plate With a Hole Under Tension
Error of strain energy in local region, relative to reference solution
GFEMgl recovers global measures accurately
Submodeling modeling does not

## Slide 8: Plate With a Hole Under Bearing Load
Expected failure
GFEMgl recovers local measures accurately
Submodeling does not
Fiber Comp.
Fiber Comp.
CMC
Plots of stress concentration through-the-thickness

## Slide 9: Plate With a Hole Under Bearing Load
Error of strain energy in local region, relative to reference solution
GFEMgl recovers global measures accurately
Submodeling does not

## Slide 10
Conclusions
Model material heterogeneity in localized region only
  Accurate local measures
  Accurate global measures
Define loading via local problem
Considerably more accurate than GL-FEM
More representative than fully homogenized model

## Slide 11
Future Work
Microstructure-informed damage
IGL-GFEMgl
Other composites