## Slide 1
Student:
Student Email:
Faculty:
Faculty Email:
AFRL Sponsor:
AFRL Directorate:
Maturation of Generalized Finite Element Technology for Multi-Scale Solid and Fluid Mechanics Applications
Javier Avecillas
javiera5@Illinois.edu
Carlos Armando Duarte
caduarte@illinois.edu
Ravi Chona
RQHF
Distribution Statement A: Approved for public release;
Distribution is unlimited. PA# AFRL-2022-4594 .

## Slide 2
Goal and challenges
Goal: Develop a computational framework able to capture localized 3-D mechanical fields on structural components.
Multiple spatial scales: From structural scale, to sub-assembly scale, panel scale, stiffener scale, spot welds and cracks.
Strategy: Non-intrusive multi-scale structural framework
Iterative Global-Local (IGL) couples structural and 3D models.
Non-intrusive feature of IGL: Combines two solvers that implement different mathematical models (shells and solids).
GFEMgl captures localized 3-D effects on a coarse mesh.
Denoted as IGL-GFEMgl
To reduce computational time, a staggered IGL-GFEMgl scheme is used where GFEMgl is applied only after IGL converges.
Lockheed Martin HTV-3X
[AFRL-RB-WP-TR-2010-3069]

## Slide 3
Generalized Finite Element Method (GFEM)
Bridging scales with global-local enrichment functions
[Babuska et al., 1994; Duarte & Oden 1995]
Discontinuous enrichment
[Moes et al., 1999]
Allows the construction of shape functions incorporating a-priori knowledge about the solution.
Enrichment functions are provided by the solution of auxiliary local boundary value problems: Global-Local enrichments functions.
Idea: Use available numerical solution to build shape functions for next step (quasi-static, transient, non-linear, etc.)
Enrichment functions are produced numerically on-the-fly through a global-local analysis.
Use a coarse mesh enriched with Global-Local (GL) functions.
GFEMgl: GFEM with global-local enrichments.
Enrichment = Numerical solutions of BVP

## Slide 4
IGL-GFEMgl: Cantilever plate with static crack
IGL-GFEMgl:
Global (Abaqus): S4 with full integration. No reinforcement at support, no crack.
Meso: HEX8, enriched with quadratic polynomials. Red nodes have global-local enrichments. Includes reinforcement at support but no crack.
Local: TET4, enriched with linear polynomials. Heaviside, and singular branch functions used to model the crack.
Global (Abaqus): 396 dofs
Meso-scale: 1980 dofs
Local: 247842 dofs
IGL
The reinforcement at the support is not included in the shell model.
Cantilever plate with static crack
Boundary conditions:
at
Material properties:
Inclined crack
Problem dimensions (unit: mm)
GFEMgl

## Slide 5
IGL-GFEMgl: Cantilever plate with static crack
IGL-GFEMgl shell-solid coupling
Excellent agreement between reference solution (DGFEA) and IGL-GFEMgl simulation.
Sub-modelling (GL-GFEMgl) overestimates the maximum displacement.

## Slide 6
IGL-GFEMgl: T-joint with static crack
IGL-GFEMgl:
Global (Abaqus): S4 with full integration. No welds.
Meso: HEX8, enriched with quadratic polynomials. Red nodes have global-local enrichments. Includes welds but no crack.
Local: TET4, enriched with quadratic polynomials, Heaviside, and singular branch functions used to model the crack.
Global (Abaqus): 4704 dofs
Meso-scale: 13008 dofs
Local: 243795 dofs
IGL
GFEMgl
The welds are not included in the shell model.
T-Joint with static crack
Boundary conditions:
at and
Material properties:
Problem dimensions (unit: in)

## Slide 7
IGL-GFEMgl: T-joint with static crack
IGL-GFEMgl shell-solid coupling
Good agreement between reference solution and IGL-GFEMgl simulation.
Sub-modelling (GL-GFEMgl) overestimates the maximum displacement.

## Slide 8
IGL-GFEM: Crack propagation and branching in a T-section beam
IGL-GFEM:
Global (Abaqus): S4 with full integration. No crack.
Local: TET4, enriched with quadratic polynomials, Heaviside, and singular branch functions used to model the crack.
There is no need for a mesoscale model. The overall structural response is captured by the global shell model while the crack propagation is performed at the local scale.
T-section with propagating crack
Boundary conditions:
Material properties:
and
Fatigue crack – Paris-Erdogan:
and
Problem dimensions (unit: in)
Global (Abaqus): 2376 dofs
Local: 249594 dofs
The crack is not included in the shell model.

## Slide 9
IGL-GFEM: Crack propagation and branching in a T-section beam
Stress Intensity Factors (SIFs) along the crack front
Crack surface at different steps
Small cracks have small influence on the overall stiffness of the T-section beam.
Conversely, larger cracks do change the stiffness of the problem.
The crack advances with a straight front.
Then, the front propagates in a shape that resembles a quarter of an ellipse.
Finally, the crack branches and continues propagating.

## Slide 10
IGL-GFEM: Crack propagation and branching in a T-section beam
Deformed configuration and :
IGL-GFEM captures the non-symmetric z−displacement field.
GL-GFEM yields a symmetric z-displacement field.
Additional metrics at the mid-height of the beam horizontal plate
IGL-GFEM captures the drop in KI. Also, the fatigue life is reasonably predicted.
Submodeling (GL-GFEM) overestimates the total life of the structure.
Conclusions
IGL addresses the challenge of connecting shells and solids elements.
Global model simulated by commercial code such as Abaqus with coarse meshes.
It is critically important to consider a two-way coupling between structural scales.