## Slide 1
Student:
Student Email:
Faculty:
Faculty Email:
AFRL Sponsor:
AFRL Directorate:
Automated topology optimization of PBF via state estimation and control of internal temperatures
Nathaniel Wood
wood.863@osu.edu
David Hoelzle
Hoelzle.1@osu.edu
Andrew Gillman
Materials and Manufacturing
Replace with University Logo
PA #:
AFRL-2022-4784

## Slide 2
[1]
Problem: Estimate the mid-build thermal physics of PBF, , with noise. Process noise is extremely complex and unmeasurable.
Process noise
Measurement noise
Process monitoring: State estimation.
Design of ?
ML techniques [5]: burden of extensive training data
DMLS = Powder Bed Fusion (PBF)
[2]
[3]
Defect: residual stresses
Measurement: IR cameras
[4]
[2] L. Cheng et. al., Additive Manufacturing, Vol. 27, 2016
[1] “DMLS Direct Metal Laser Sintering by FORECAST 3D”.
[5] Gaikwad et. al. IISE Transactions, 2020
[3] Wood et. al. SFF 2019, pp. 1445-1481
[4] DeBroy et. al. Progress in Material Science, 2018
Motivation
PA #:
AFRL-2022-4784
Project goal: Estimate PBF thermal physics without using training data.

## Slide 3
Strategy: Ensemble Kalman filter
input(t)=u(t)
1
2
3
4
Thermal camera
Mathematical model predicts unmeasured temperatures
Model
input(t)
Estimates at all nodes
Isolate output estimates
Output estimation error
Use feedback action to guarantee convergence of estimates to unknown true values
Measured
Process Noise
Measurement Noise
Estimation feedback strategy: Ensemble Kalman filter [1]
IDs Gaussian distributions closest to and
is 2-norm optimal estimate wrt to this noise estimate
No a priori knowledge needed
x
z
[1] Evensen, G. Ocean Dynamics, 2003
PA #:
AFRL-2022-4784

## Slide 4
Project thrusts
Simulation-based validation of state estimation algorithm
  True process measurements replaced by simulated measurements from a more accurate process model than that used by state estimator
  Assess accuracy with respect to simulated ground truth, in terms of 2-norm and -norm error signals.
  Rapid algorithm testing and refinement.
Gathering experimental data of PBF internal temperature response, associated input/output signals
  Utilization of open architecture PBF machine at ARCTOS, Dayton OH.
  Validation of state estimator algorithm with experimental data.
  Gathering microstructural data to test correlation of estimated temperature field to features of interest.
PA #:
AFRL-2022-4784
2750-A Indian Ripple Rd, Beavercreek, OH 45440
3D spatial coordinate

## Slide 5
Open architecture machine, sample geometries
PA #:
AFRL-2022-4784
ScanLab intelliSCAN 20 galvanometers + RTC5 card
IPG YLR-500-SM laser source
Optris PI 640i off axis IR camera
Custom-filtered Sony IMX174 coaxial camera

## Slide 6
Summary: collected data streams
PA #:
AFRL-2022-4784
Thermocouple (TC) signals, embedded within test samples (x4 per sample)
TC signal, embedded within build plate
Micrographs of generated build footprints, and of single scan tracks
Real-time X,Y galvanometer commanded positions
Real-time laser power
Real-time laser trigger signal
Set point of beam diameter
Images from off-axis IR camera
Images from coaxial camera
Ground-truth validation data for PBF thermal models.
Real-time process inputs, used to generate accurate process models.
Real-time process outputs, used in process monitoring algorithms.

## Slide 7
Experimental procedures
PA #:
AFRL-2022-4784
42.5 and 63.75 W, 3 sweeps
150 W, 3 sweeps
150 W, 1 sweep

## Slide 8
Sample TC data
PA #:
AFRL-2022-4784
Sample 1
Sample 6
Net motion of laser across the sample lengths between multiple sweeps is what produces 2 local maxima for TCA, and one local maximum for TCB.

## Slide 9
Sample on axis camera data
PA #:
AFRL-2022-4784
Camera calibrated by comparing imaged melt pool widths against ground truth microscope data for all powers examined.
Ghost image due to slight misalignment of optical train.
Background noise eliminated via thresholding.
Ghost image removed via watershed filtering the distance transform complement of the eroded, binarized image.
Colormap: K. Moreland, Proceedings HVEI, 2016

## Slide 10
Conclusions and acknowledgements
PA #:
AFRL-2022-4784
Conclusions
We have gathered an exhaustive dataset that samples mid-build internal PBF temperatures under a variety of processing conditions, together with industry-relevant process input and output signatures.
We intend to make this dataset freely available to the community and will announce its location in a future publication.
We intend to use this data to validate Ensemble Kalman Filter-based estimations of PBF temperature fields, which will be a step towards achieving PBF process monitoring without the need for extensive training data. This will complete thrusts 1 and 2 of this research project.
Acknowledgements
My advisor and AFRL sponsor, David Hoelzle and Andrew Gillman, respectively
My peers in the Hoelzle Research Lab
Open Additive staff, especially John Middendorf for their expertise and machine
Professor Prasad Mokashi for his help with FEM theory